https://online.tugraz.at/tug_online/voe_main2.getvolltext?pCurrPk=77938
http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.prd29-genc-009492c/ch05s02s01.html

The secure operating system is responsible for security critical operations.
Mostly cryptographic material is stored in the TZ and protected by its secu-
rity mechanisms. The secure OS is part of the TCB of the whole system and
therefore should be kept as small as possible. The secure OS also has to host
the normal OS. In the boot process of a TrustZone aware system the secure OS
boots up first and then the secure OS boots up the normal world operating
system. Therefore acting as a boot loader for the normal world.
Both worlds need to communicate with each other, to implement a RPC mech-
anisms. The world communication is designed to work similar to an operating
system call. A special operation mode exists in the TZ, which allows the cur-
rent Central processing unit (CPU) to switch its state. This mode is called
monitor mode and is implemented by the ANDIX OS. In this mode the sys-
tem can switch between the two worlds. Both worlds can access this monitor
mode by calling a trapdoor instruction called secure Monitor Call (SMC). This
instruction works like to a software interrupt, which traps the user space into
the kernel space, the SMC traps the kernel mode into the monitor mode. Infor-
mation can be transferred to the monitor mode, by setting up the CPU registers
before executing the SMC instruction. These registers can then be read in the
monitor mode.

user/kernel space
In modern operating systems the kernel and user applica-
tions are executed in different operating modes of the Central processing
unit (CPU). This isolates the kernel and user application from one another
and protects the system from faulty and malicious applications.
system call
A system call is a mechanism for applications running in the user
space to utilize functions that are only available in the kernel space. The
kernel exposes a system call interface and allows application to use these
functions.
interrupt
Interrupts the processor in its current execution and notifies the pro-
cessor about the occurred event, by jumping to the handler address.
System-on-a-Chip
A System on Chip (SoC) is a system where its components
are integrated into one circuit. Modern smart phones are also SoCs.
secure world
The ARM TrustZone partitions the SoC into two partitions. The
partition of the SoC which is protected by the ARM TrustZone is called
secure world
normal world
The ARM TrustZone partitions the SoC into two partitions. The
partition of the SoC which is not the secure world is called normal world
rich operating system
A rich operating system is an operating system capable
of providing a rich user interface. In this thesis we will refer to a rich
operating system as the operating system running in the normal world
and providing the normal user interface

An ARM processor can operate in different modes. The current mode deter-
mines the privilege level of the current operation. In the ARM architecture up
to three privilege levels are available. Table

show which ARM mode has
which privilege level.
.: ARM Modes and privilege levels
privilege level ARM Mode
PL0	User
PL1	System
PL1 Supervisor
PL1	FIQ
PL1	IRQ
PL1 Abort
PL1 Monitor
PL2 Hyp

The privilege levels determine the current access rights to some features of the
system. PL
0
is the privilege level for unprivileged executions. PL
1
gives access
to all features of the system except virtualization features. PL
2
gives access to
all features of the system including the virtualization features. PL
0
usually is
15
2. Preliminaries
used for user applications. PL
1
usually is used by operating system kernels
and PL
2
is used for hypervisors like Xen
2
.

igure
2
.
3
shows the boot process of an ARM TZ aware system. After the de-
vice is powered on, a first stage boot loader is loaded from read only memory.
This first stage boot loader is the ROM SoC Bootloader in figure
2
.
3
. This boot
loader tries to load the secure world OS from a known location. This could be
a memory card, on board flash memory or a network device. The secure world
OS is digitally signed by the device manufacturer. This signature is verified by
the first stage boot loader. It uses a public key for the signature verification,
stored in a read only memory on the SoC. It is essential for the security in
terms of origin integrity that this key can not be modified. The mechanisms
for keeping this key secure depend on the SoC. We can only trust that this key
is not modified. When the signature can be verified successfully, the secure
world OS is executed. The secure world OS boots up and than verifies and ex-
ecutes the normal world boot loader in the normal world. This again loads and
executes the normal world OS. These process description is an abstraction of a
real world secure boot process. The process details may differ from platform
to platform.